## Slide 1: WM-400L Beaglebone Black Shield
Gerson Fernando Budke
nandojve@gmail.com

## Slide 2: Agenda
Overview
Requirements
Play with QTouch
Configure Bleaglebone Black
Serial port demo
Issues?

## Slide 3: Overview
The hands on target is provide basic knowledge to use WM-400L Beaglebone Black Shield (BBS) with Beaglebone Black as Host. A Qtouch demo will be presented to advance knowledge about test and programming the board.

## Slide 4: Requirements
To complete this Hands On you need:
  Complete ATMEL Studio Hands On
  Must have a WM-400L BBS
  Must have a Beaglebone Black
  A PC that run SAM-BA bootloader
  A PC with ARM GCC

## Slide 5: Play with QTouch
Play is only to remember how to compile and download firmware to WM Series with ARM microcontroller, so can step over.

## Slide 6: Play with QTouch
Unplug Beaglebone Black from KIT
Access Qtouch demo in <asf dir>\backport\WM400\Qtouch
Build demo code
Run SAM-BA bootloader and upload firmware
Quit SAM-BA bootloader IDE
Restart board
Pressing DFU switch enable LED2
And disable LED1. Unpressing toggle LED0 & LED1
Pressing QT_BTN will enabled LED0 and unpressing disable

## Slide 7: Configure Bleaglebone Black
Unplug WM-400 module
Plug Beaglebone into PC and wait until mass storage be mount.
Open uEnv.txt to change boot definition to enable ttyO1 to communicate with WM-400 module

## Slide 8: Configure Bleaglebone Black
Add capemgr.enable_partno= variable with:
  BB-UART1,
  BB-I2C2
save

## Slide 9: Configure Bleaglebone Black
To access linux open putty terminal with Gadget Serial Port

## Slide 10: Configure Bleaglebone Black
Press enter
Beaglebone Black will show Angstrom logo
Use root to login
Type “halt”
Close putty
Wait until leds off
Unplug Beaglebone USB cable

## Slide 11: Configure Bleaglebone Black
Connect WM-400 to Beaglebone
Plug Beaglebone USB cable
Wait until mass storage be mounted
Repeat the putty process to access linux
Now, Type “ls /dev/ttyO*” to see serial port 1 was enabled

## Slide 12: Configure Bleaglebone Black
In PC:
  Write the follow script in notepad
  Select ALL and Copy to transfer area
In Putty Shell:
  Type “vim gpio.sh”
  Type “i”
  Type “SHIFT Insert”
  Type “ESC”
  Type “:x!”
  Type “chmod 755 gpio.sh”

## Slide 13: Configure Bleaglebone Black
Type “./gpio.sh”
This script will configure:
  GPIO to Reset board
  GPIO to Power Management
  ttyO1 speed to 115200 8N1
WM-400 will start after running gpio.sh

## Slide 14: Configure Bleaglebone Black
Reset sequence:
echo 0 > /sys/class/gpio/gpio60/value
  This reset WM-400 board
echo 1 > /sys/class/gpio/gpio60/value
  This start WM-400 board
The DFU button is represented by gpio26. If you need simulated a button press proceed like reset sequence change gpio60 to gpio26

## Slide 15: Serial port demo
Plug WM-400 USB cable
Access USART_BBBS demo in <asf dir>\backport\WM400\USART_BBBS
Build demo code
Use GPIOs to simulated SAM-BA DFU sequence
Run SAM-BA bootloader and upload firmware
Quit SAM-BA bootloader IDE
Use GPIOs to reset board
Type “cat /dev/ttyO1” to see what WM-400 send to Beaglebone
“CTRL+C” to quit demo
“halt” to shutdown linux

## Slide 16: Issues?
nandojve at gmail dot com